## Slide 1: Chapter 4
The Processor

## Slide 2: Introduction
CPU performance factors
  Instruction count
    Determined by ISA and compiler
  CPI and Cycle time
    Determined by CPU hardware
We will examine two MIPS implementations
  A simplified version
  A more realistic pipelined version
Simple subset, shows most aspects
  Memory reference: lw, sw
  Arithmetic/logical: add, sub, and, or, slt
  Control transfer: beq, j
§4.1 Introduction

## Slide 3: Instruction Execution
PC  instruction memory, fetch instruction
Register numbers  register file, read registers
Depending on instruction class
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch target address
  Access data memory for load/store
  PC  target address or PC + 4

## Slide 4: CPU Overview

## Slide 5: Multiplexers
Can’t just join wires together
  Use multiplexers

## Slide 6: Control

## Slide 7: Logic Design Basics
§4.2 Logic Design Conventions
Information encoded in binary
  Low voltage = 0, High voltage = 1
  One wire per bit
  Multi-bit data encoded on multi-wire buses
Combinational element
  Operate on data
  Output is a function of input
State (sequential) elements
  Store information

## Slide 8: Combinational Elements
AND-gate
  Y = A & B
A
B
Y
I0
I1
Y
M u x
S
Multiplexer
  Y = S ? I1 : I0
A
B
Y
+
A
B
Y
ALU
F
Adder
  Y = A + B
Arithmetic/Logic Unit
  Y = F(A, B)

## Slide 9: Sequential Elements
Register: stores data in a circuit
  Uses a clock signal to determine when to update the stored value
  Edge-triggered: update when Clk changes from 0 to 1
D
Clk
Q
Clk
D
Q

## Slide 10: Sequential Elements
Register with write control
  Only updates on clock edge when write control input is 1
  Used when stored value is required later
D
Clk
Q
Write
Write
D
Q
Clk

## Slide 11: Clocking Methodology
Combinational logic transforms data during clock cycles
  Between clock edges
  Input from state elements, output to state element
  Longest delay determines clock period

## Slide 12: Building a Datapath
Datapath
  Elements that process data and addresses in the CPU
    Registers, ALUs, mux’s, memories, …
We will build a MIPS datapath incrementally
  Refining the overview design
§4.3 Building a Datapath

## Slide 13: Instruction Fetch
32-bit register
Increment by 4 for next instruction

## Slide 14: R-Format Instructions
Read two register operands
Perform arithmetic/logical operation
Write register result

## Slide 15: Load/Store Instructions
Read register operands
Calculate address using 16-bit offset
  Use ALU, but sign-extend offset
Load: Read memory and update register
Store: Write register value to memory

## Slide 16: Branch Instructions
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 2 places (word displacement)
  Add to PC + 4
    Already calculated by instruction fetch

## Slide 17: Branch Instructions
Just re-routes wires
Sign-bit wire replicated

## Slide 18: Composing the Elements
First-cut data path does an instruction in one clock cycle
  Each datapath element can only do one function at a time
  Hence, we need separate instruction and data memories
Use multiplexers where alternate data sources are used for different instructions

## Slide 19: R-Type/Load/Store Datapath

## Slide 20: Full Datapath

## Slide 21: ALU Control
ALU used for
  Load/Store: F = add
  Branch: F = subtract
  R-type: F depends on funct field
§4.4 A Simple Implementation Scheme
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | set-on-less-than
1100 | NOR

## Slide 22: ALU Control
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
opcode | ALUOp | Operation | funct | ALU function | ALU control
lw | 00 | load word | XXXXXX | add | 0010
sw | 00 | store word | XXXXXX | add | 0010
beq | 01 | branch equal | XXXXXX | subtract | 0110
R-type | 10 | add | 100000 | add | 0010
 |  | subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001
 |  | set-on-less-than | 101010 | set-on-less-than | 0111

## Slide 23: The Main Control Unit
Control signals derived from instruction
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0
4
rs
rt
address
31:26
25:21
20:16
15:0
R-type
Load/ Store
Branch
opcode
always read
read, except for load
write for R-type and load
sign-extend and add

## Slide 24: Datapath With Control

## Slide 25: R-Type Instruction

## Slide 26: Load Instruction

## Slide 27: Branch-on-Equal Instruction

## Slide 28: Implementing Jumps
Jump uses word address
Update PC with concatenation of
  Top 4 bits of old PC
  26-bit jump address
  00
Need an extra control signal decoded from opcode
2
address
31:26
25:0
Jump

## Slide 29: Datapath With Jumps Added

## Slide 30: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary period for different instructions
Violates design principle
  Making the common case fast
We will improve performance by pipelining

## Slide 31: Pipelining Analogy
Pipelined laundry: overlapping execution
  Parallelism improves performance
§4.5 An Overview of Pipelining
Four loads:
  Speedup = 8/3.5 = 2.3
Non-stop:
  Speedup ≈ number of stages

## Slide 32: MIPS Pipeline
Five stages, one step per stage
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access memory operand
  WB: Write result back to register

## Slide 33: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 34: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)

## Slide 35: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructionspipelined = Time between instructionsnonpipelined Number of stages
  In our example, 800/5 = 160ps
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease

## Slide 36: Pipeline Speedup
Our example with 3 instructions
  Tpipelined = 1400ps
  Tnopipelined = 2400ps
  Speedup = 2400/1400 = 1.714
Add 1,000,000 instructions
  Tpipelined = 1,000,000 * 200 + 1400
  Tnopipelined = 1,000,000 * 800 + 2400
  Speedup = 800,002,400/200,001,400 = 4

## Slide 37: Pipelining and ISA Design
MIPS ISA designed for pipelining
  All instructions are 32-bits
    Easier to fetch and decode in one cycle
    c.f. x86: 1- to 17-byte instructions
  Few and regular instruction formats
    Can decode and read registers in one step
  Load/store addressing
    Can calculate address in 3rd stage, access memory in 4th stage
  Alignment of memory operands
    Memory access takes only one cycle

## Slide 38: Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 39: Structure Hazards
Conflict for use of a resource
In MIPS pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches

## Slide 40: Data Hazards
An instruction depends on completion of data access by a previous instruction
  add $s0, $t0, $t1 sub $t2, $s0, $t3

## Slide 41: Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath

## Slide 42: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!

## Slide 43: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F;
A(12), B(0), E(4), C(16), F(8)
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
11 cycles
13 cycles

## Slide 44: Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
In MIPS pipeline
  Need to compare registers and compute target early in the pipeline
  Add hardware to do it in ID stage

## Slide 45: Stall on Branch
Wait until branch outcome determined before fetching next instruction

## Slide 46: Branch Prediction
Longer pipelines can’t readily determine branch outcome early
  Stall penalty becomes unacceptable
Predict outcome of branch
  Only stall if prediction is wrong
In MIPS pipeline
  Can predict branches not taken
  Fetch instruction after branch, with no delay

## Slide 47: MIPS with Predict Not Taken
Prediction correct
Prediction incorrect

## Slide 48: More-Realistic Branch Prediction
Static branch prediction
  Based on typical branch behavior
  Example: loop and if-statement branches
    Predict backward branches taken
    Predict forward branches not taken
Dynamic branch prediction
  Hardware measures actual branch behavior
    e.g., record recent history of each branch
  Assume future behavior will continue the trend
    When wrong, stall while re-fetching, and update history

## Slide 49: Pipeline Summary
Pipelining improves performance by increasing instruction throughput
  Executes multiple instructions in parallel
  Each instruction has the same latency
Subject to hazards
  Structure, data, control
Instruction set design affects complexity of pipeline implementation
The BIG Picture

## Slide 50: MIPS Pipelined Datapath
§4.6 Pipelined Datapath and Control
WB
MEM
Right-to-left flow leads to hazards

## Slide 51: Pipeline registers
Need registers between stages
  To hold information produced in previous cycle

## Slide 52: Pipeline Operation
Cycle-by-cycle flow of instructions through the pipelined datapath
  “Single-clock-cycle” pipeline diagram
    Shows pipeline usage in a single cycle
    Highlight resources used
  c.f. “multi-clock-cycle” diagram
    Graph of operation over time
We’ll look at “single-clock-cycle” diagrams for load & store

## Slide 53: IF for Load, Store, …

## Slide 54: ID for Load, Store, …

## Slide 55: EX for Load

## Slide 56: MEM for Load

## Slide 57: WB for Load
Wrong register number

## Slide 58: Corrected Datapath for Load

## Slide 59: EX for Store

## Slide 60: MEM for Store

## Slide 61: WB for Store

## Slide 62: Multi-Cycle Pipeline Diagram
Form showing resource usage

## Slide 63: Multi-Cycle Pipeline Diagram
Traditional form

## Slide 64: Single-Cycle Pipeline Diagram
State of pipeline in a given cycle

## Slide 65: Pipelined Control (Simplified)

## Slide 66: Pipelined Control
Control signals derived from instruction
  As in single-cycle implementation

## Slide 67: Pipelined Control

## Slide 68: Data Hazards in ALU Instructions
Consider this sequence:
  sub $2, $1,$3 and $12,$2,$5 or $13,$6,$2 add $14,$2,$2 sw $15,100($2)
We can resolve hazards with forwarding
  How do we detect when to forward?
§4.7 Data Hazards: Forwarding vs. Stalling

## Slide 69: Dependencies & Forwarding

## Slide 70: Detecting the Need to Forward
Pass register numbers along pipeline
  e.g., ID/EX.RegisterRs = register number for Rs sitting in ID/EX pipeline register
ALU operand register numbers in EX stage are given by
  ID/EX.RegisterRs, ID/EX.RegisterRt
Data hazards when
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRs
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRt
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRs
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRt
Fwd from EX/MEM pipeline reg
Fwd from MEM/WB pipeline reg

## Slide 71: Dependence Detection
sub-and – type 1a hazard
sub-or – type 2b hazard
sub-add – no hazard
sub-sw – no hazard

## Slide 72: Detecting the Need to Forward
But only if forwarding instruction will write to a register!
  EX/MEM.RegWrite, MEM/WB.RegWrite
And only if Rd for that instruction is not $zero
  EX/MEM.RegisterRd ≠ 0, MEM/WB.RegisterRd ≠ 0

## Slide 73: Forwarding Paths

## Slide 74: Forwarding Conditions
EX hazard
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs)) ForwardA = 10
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRt)) ForwardB = 10
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01

## Slide 75: Double Data Hazard
Consider the sequence:
  add $1,$1,$2 add $1,$1,$3 add $1,$1,$4
Both hazards occur
  Want to use the most recent
Revise MEM hazard condition
  Only fwd if EX hazard condition isn’t true

## Slide 76: Revised Forwarding Condition
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs)) and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRt)) and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01

## Slide 77: Datapath with Forwarding

## Slide 78: Load-Use Data Hazard
Need to stall for one cycle

## Slide 79: Load-Use Hazard Detection
Check when using instruction is decoded in ID stage
ALU operand register numbers in ID stage are given by
  IF/ID.RegisterRs, IF/ID.RegisterRt
Load-use hazard when
  ID/EX.MemRead and ((ID/EX.RegisterRt = IF/ID.RegisterRs) or (ID/EX.RegisterRt = IF/ID.RegisterRt))
If detected, stall and insert bubble

## Slide 80: How to Stall the Pipeline
Force control values in ID/EX register to 0
  EX, MEM and WB do nop (no-operation)
Prevent update of PC and IF/ID register
  Using instruction is decoded again
  Following instruction is fetched again
  1-cycle stall allows MEM to read data for lw
    Can subsequently forward to EX stage

## Slide 81: Stall/Bubble in the Pipeline
Stall inserted here

## Slide 82: Stall/Bubble in the Pipeline
Or, more accurately…

## Slide 83: Datapath with Hazard Detection

## Slide 84: Stalls and Performance
Stalls reduce performance
  But are required to get correct results
Compiler can arrange code to avoid hazards and stalls
  Requires knowledge of the pipeline structure
The BIG Picture

## Slide 85: Branch Hazards
If branch outcome determined in MEM
§4.8 Control Hazards
PC
Flush these instructions
(Set control values to 0)

## Slide 86: Reducing Branch Delay
Move hardware to determine outcome to ID stage
  Target address adder
  Register comparator
Example: branch taken
  36: sub $10, $4, $8 40: beq $1, $3, 7 44: and $12, $2, $5 48: or $13, $2, $6 52: add $14, $4, $2 56: slt $15, $6, $7 ... 72: lw $4, 50($7)

## Slide 87: Data Hazards for Branches
If a comparison register is a destination of 2nd or 3rd preceding ALU instruction
…
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
add $4, $5, $6
add $1, $2, $3
beq $1, $4, target
Can resolve using forwarding

## Slide 88: Data Hazards for Branches
If a comparison register is a destination of preceding ALU instruction or 2nd preceding load instruction
  Need 1 stall cycle
beq stalled
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
ID
EX
MEM
WB
add $4, $5, $6
lw $1, addr
beq $1, $4, target

## Slide 89: Data Hazards for Branches
If a comparison register is a destination of immediately preceding load instruction
  Need 2 stall cycles
beq stalled
IF
ID
EX
MEM
WB
IF
ID
ID
ID
EX
MEM
WB
beq stalled
lw $1, addr
beq $1, $0, target

## Slide 90: Dynamic Branch Prediction
In deeper and superscalar pipelines, branch penalty is more significant
Use dynamic prediction
  Branch prediction buffer (aka branch history table)
  Indexed by recent branch instruction addresses
  Stores outcome (taken/not taken)
  To execute a branch
    Check table, expect the same outcome
    Start fetching from fall-through or target
    If wrong, flush pipeline and flip prediction

## Slide 91: 1-Bit Predictor: Shortcoming
Inner loop branches mispredicted twice!
outer: … … inner: …
…
beq …, …, inner … beq …, …, outer
  Mispredict as taken on last iteration of inner loop
  Then mispredict as not taken on first iteration of inner loop next time around

## Slide 92: 2-Bit Predictor
Only change prediction on two successive mispredictions

## Slide 93: Calculating the Branch Target
Even with predictor, still need to calculate the target address
  1-cycle penalty for a taken branch
Branch target buffer
  Cache of target addresses
  Indexed by PC when instruction fetched
    If hit and instruction is branch predicted taken, can fetch target immediately

## Slide 94: Instruction-Level Parallelism (ILP)
Pipelining: executing multiple instructions in parallel
To increase ILP
  Deeper pipeline
    Less work per stage  shorter clock cycle
  Multiple issue
    Replicate pipeline stages  multiple pipelines
    Start multiple instructions per clock cycle
    CPI < 1, so use Instructions Per Cycle (IPC)
    E.g., 4GHz 4-way multiple-issue
      16 BIPS, peak CPI = 0.25, peak IPC = 4
    But dependencies reduce this in practice
§4.10 Parallelism via Instructions

## Slide 95: Multiple Issue
Static multiple issue
  Compiler groups instructions to be issued together
  Packages them into “issue slots”
  Compiler detects and avoids hazards
Dynamic multiple issue
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime

## Slide 96: Speculation
“Guess” what to do with an instruction
  Start operation as soon as possible
  Check whether guess was right
    If so, complete the operation
    If not, roll-back and do the right thing
Common to static and dynamic multiple issue
Examples
  Speculate on branch outcome
    Roll back if path taken is different
  Speculate on load
    Roll back if location is updated

## Slide 97: Compiler/Hardware Speculation
Compiler can reorder instructions
  e.g., move load before branch
  Can include “fix-up” instructions to recover from incorrect guess
Hardware can look ahead for instructions to execute
  Buffer results until it determines they are actually needed
  Flush buffers on incorrect speculation

## Slide 98: Static Multiple Issue
Compiler groups instructions into “issue packets”
  Group of instructions that can be issued on a single cycle
  Determined by pipeline resources required
Think of an issue packet as a very long instruction
  Specifies multiple concurrent operations
   Very Long Instruction Word (VLIW)

## Slide 99: Scheduling Static Multiple Issue
Compiler must remove some/all hazards
  Reorder instructions into issue packets
  No dependencies with a packet
  Possibly some dependencies between packets
    Varies between ISAs; compiler must know!
  Pad with nop if necessary

## Slide 100: MIPS with Static Dual Issue
Two-issue packets
  One ALU/branch instruction
  One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop
Address | Instruction type | Pipeline Stages |  |  |  |  |  | 
n | ALU/branch | IF | ID | EX | MEM | WB |  | 
n + 4 | Load/store | IF | ID | EX | MEM | WB |  | 
n + 8 | ALU/branch |  | IF | ID | EX | MEM | WB | 
n + 12 | Load/store |  | IF | ID | EX | MEM | WB | 
n + 16 | ALU/branch |  |  | IF | ID | EX | MEM | WB
n + 20 | Load/store |  |  | IF | ID | EX | MEM | WB

## Slide 101: MIPS with Static Dual Issue

## Slide 102: Hazards in the Dual-Issue MIPS
More instructions executing in parallel
EX data hazard
  Forwarding avoided stalls with single-issue
  Now can’t use ALU result in load/store in same packet
    add $t0, $s0, $s1 load $s2, 0($t0)
    Split into two packets, effectively a stall
Load-use hazard
  Still one cycle use latency, but now two instructions
More aggressive scheduling required

## Slide 103: Scheduling Example
Schedule this for dual-issue MIPS
Loop: lw $t0, 0($s1) # $t0=array element addu $t0, $t0, $s2 # add scalar in $s2 sw $t0, 0($s1) # store result addi $s1, $s1,–4 # decrement pointer bne $s1, $zero, Loop # branch $s1!=0
 | ALU/branch | Load/store | cycle
Loop: | nop | lw $t0, 0($s1) | 1
 | addi $s1, $s1,–4 | nop | 2
 | addu $t0, $t0, $s2 | nop | 3
 | bne $s1, $zero, Loop | sw $t0, 4($s1) | 4
  IPC = 5/4 = 1.25 (c.f. peak IPC = 2)

## Slide 104: Loop Unrolling
Replicate loop body to expose more parallelism
  Reduces loop-control overhead
Use different registers per replication
  Called “register renaming”
  Avoid loop-carried “anti-dependencies”
    Store followed by a load of the same register
    Aka “name dependence”
      Reuse of a register name

## Slide 105: Loop Unrolling Example
IPC = 14/8 = 1.75
  Closer to 2, but at cost of registers and code size
 | ALU/branch | Load/store | cycle
Loop: | addi $s1, $s1,–16 | lw $t0, 0($s1) | 1
 | nop | lw $t1, 12($s1) | 2
 | addu $t0, $t0, $s2 | lw $t2, 8($s1) | 3
 | addu $t1, $t1, $s2 | lw $t3, 4($s1) | 4
 | addu $t2, $t2, $s2 | sw $t0, 16($s1) | 5
 | addu $t3, $t4, $s2 | sw $t1, 12($s1) | 6
 | nop | sw $t2, 8($s1) | 7
 | bne $s1, $zero, Loop | sw $t3, 4($s1) | 8

## Slide 106: Dynamic Multiple Issue
“Superscalar” processors
CPU decides whether to issue 0, 1, 2, … each cycle
  Avoiding structural and data hazards
Avoids the need for compiler scheduling
  Though it may still help
  Code semantics ensured by the CPU

## Slide 107: Dynamic Pipeline Scheduling
Allow the CPU to execute instructions out of order to avoid stalls
  But commit result to registers in order
Example
  lw $t0, 20($s2) addu $t1, $t0, $t2 sub $s4, $s4, $t3 slti $t5, $s4, 20
  Can start sub while addu is waiting for lw

## Slide 108: Dynamically Scheduled CPU
Results also sent to any waiting reservation stations
Reorders buffer for register writes
Can supply operands for issued instructions
Preserves dependencies
Hold pending operands

## Slide 109: Why Do Dynamic Scheduling?
Why not just let the compiler schedule code?
Not all stalls are predicable
  e.g., cache misses
Can’t always schedule around branches
  Branch outcome is dynamically determined
Different implementations of an ISA have different latencies and hazards

## Slide 110: Does Multiple Issue Work?
Yes, but not as much as we’d like
Programs have real dependencies that limit ILP
Some dependencies are hard to eliminate
  e.g., pointer aliasing
Some parallelism is hard to expose
  Limited window size during instruction issue
Memory delays and limited bandwidth
  Hard to keep pipelines full
Speculation can help if done well
The BIG Picture

## Slide 111: Power Efficiency
Complexity of dynamic scheduling and speculations requires power
Multiple simpler cores may be better
Microprocessor | Year | Clock Rate | Pipeline Stages | Issue width | Out-of-order/ Speculation | Cores | Power
i486 | 1989 | 25MHz | 5 | 1 | No | 1 | 5W
Pentium | 1993 | 66MHz | 5 | 2 | No | 1 | 10W
Pentium Pro | 1997 | 200MHz | 10 | 3 | Yes | 1 | 29W
P4 Willamette | 2001 | 2000MHz | 22 | 3 | Yes | 1 | 75W
P4 Prescott | 2004 | 3600MHz | 31 | 3 | Yes | 1 | 103W
Core | 2006 | 2930MHz | 14 | 4 | Yes | 2 | 75W
UltraSparc III | 2003 | 1950MHz | 14 | 4 | No | 1 | 90W
UltraSparc T1 | 2005 | 1200MHz | 6 | 1 | No | 8 | 70W

## Slide 112: Cortex A8 and Intel i7
Processor | ARM A8 | Intel Core i7 920
Market | Personal Mobile Device | Server, cloud
Thermal design power | 2 Watts | 130 Watts
Clock rate | 1 GHz | 2.66 GHz
Cores/Chip | 1 | 4
Floating point? | No | Yes
Multiple issue? | Dynamic | Dynamic
Peak instructions/clock cycle | 2 | 4
Pipeline stages | 14 | 14
Pipeline schedule | Static in-order | Dynamic out-of-order with speculation
Branch prediction | 2-level | 2-level
1st level caches/core | 32 KiB I, 32 KiB D | 32 KiB I, 32 KiB D
2nd level caches/core | 128-1024 KiB | 256 KiB
3rd level caches (shared) | - | 2- 8 MB
§4.11 Real Stuff: The ARM Cortex-A8 and Intel Core i7 Pipelines

## Slide 113: ARM Cortex-A8 Pipeline

## Slide 114: ARM Cortex-A8 Performance

## Slide 115: Core i7 Pipeline

## Slide 116: Core i7 Performance

## Slide 117: Fallacies
Pipelining is easy (!)
  The basic idea is easy
  The devil is in the details
    e.g., detecting data hazards
Pipelining is independent of technology
  So why haven’t we always done pipelining?
  More transistors make more advanced techniques feasible
  Pipeline-related ISA design needs to take account of technology trends
    e.g., predicated instructions
§4.14 Fallacies and Pitfalls

## Slide 118: Pitfalls
Poor ISA design can make pipelining harder
  e.g., complex instruction sets (VAX, IA-32)
    Significant overhead to make pipelining work
    IA-32 micro-op approach
  e.g., complex addressing modes
    Register update side effects, memory indirection
  e.g., delayed branches
    Advanced pipelines have long delay slots

## Slide 119: Concluding Remarks
ISA influences design of datapath and control
Datapath and control influence design of ISA
Pipelining improves instruction throughput using parallelism
  More instructions completed per second
  Latency for each instruction not reduced
Hazards: structural, data, control
Multiple issue and dynamic scheduling (ILP)
  Dependencies limit achievable parallelism
  Complexity leads to the power wall
§4.14 Concluding Remarks